## Slide 1: Let’s Blink a LED (in C++, of course)
Wouter van Ooijen
wouter.vanooijen@hu.nl, wouter@voti.nl
Lecturer at HBO-ICT, Computer Science, Utrecht, Netherlands
Occasional speaker (Meeting C++, EmBo++, CoreHard, Accu, …)
Embedded C++ promoter (both embedded and C++ seem to disagree…)
www.github.com/wovo/talk-gpio-abstractions
Warning: there will be code….
HBO-ICT

## Slide 2: Why blink a LED?
“Hello world” of mico-controller programming
Illustrates low-level abstraction (how to pass a GPIO pin)

## Slide 3: What is a micro-controller?
Single-chip computer: CPU, code memory, data memory, I/O
Programmed without a traditional OS (Linux doesn’t fit, yet)
IDE and build on a laptop
Download to target micro-controller, run
Very wide range:
 | Price | Flash | RAM | MIPS
Ultra-low cost | 0.03 | 256 b | 16 b | 1
‘standard’ 8-bit | 0.50 | 16 Kb | 2 Kb | 16
Cortex 32-bit | 2.00 | 1 Mb | 100 Kb | 100

## Slide 4: What is a GPIO?
General Purpose Input Output pin
Electrical connection (pin) under direct application control
Can be used as input, or as output
Operations:
  Make it an input
    Read the value (pushbutton)
  Make it an output
    Write a value to it (LED)
Up after write( 1 )
Low after write( 0 )
Open for input,
Closed for output

## Slide 5: Blink a LED
Using the Arduino Uno
AtMega328 micro-controller
  Atmel, now Microchip
  AVR8 CPU, 16 MIPS
  8 bit CPU, 16 bit address range
  Hardvard architecture: separate data and instruction memories
  8k Flash, 2K ROM
  C++20 compiler: https://github.com/CrustyAuklet/avr-libstdcxx/releases
Onboard LED
USB connection for download and (debug) logging
Extremely cheap, well-doucmented, and widely available
Has its own libraries and IDE (which I both hate)

## Slide 6: Arduino Uno onboard LED
Connected to PB5 = PORT B, pin 5

## Slide 7: Memory mapped I/O
Data memory contains RAM, but also hardware registers
AtMega328P datasheet (294 pages):

## Slide 8: Acessing memory-mapped registers
LED at PORT B, pin 5
DDRB at 0x24
PORTB at 0x25
Cast the values to const pointers
Must be volatile
// pointer to the Data Direction Register for port B
auto const DDRB = reinterpret_cast< volatile uint8_t * >( 0x24 );
// pointer to the Data Register for port B
auto const PORTB = reinterpret_cast< volatile uint8_t * >( 0x25 );

## Slide 9: Changing (only) bit 5
Value with only bit 5 set: 0b0010’0000
But I prefer ( 0b01 << 5 )
Make a bit high (1): | operator
Make a bit low (0): & operator with inverted value (~ operator)
  ( ~ 0b0010’0000 ) = 0b1101’1111
Compound assignments ( |= operator ) to a volatile are deprecated in C++20 (might be rectified in C++23…)
// make PORTB pin 5 high
*PORTB = *PORTB | ( 0b01 << 5 );
// make PORTB pin 5 low
*PORTB = *PORTB & ~ ( 0b01 << 5 );

## Slide 10: Wait some time
Loop a (large) number of times
Beware: int on an AVR8 is only 16 bits
Loop must be something that prevents optimizing the loop away
// wait a while
for( uint32_t i = 0; i < 500'000; ++i ){
asm( "nop" );
}

## Slide 11: Full blink code
#include <cstdint>
// pointers to DDRB and PORTB
auto const DDRB = reinterpret_cast< volatile uint8_t * >( 0x24 );
auto const PORTB = reinterpret_cast< volatile uint8_t * >( 0x25 );
int main( void ){
*DDRB = *DDRB | ( 0b01 << 5 ); // make PORTB pin 5 an output
for(;;){
*PORTB = *PORTB | ( 0b01 << 5 ); // make PORTB pin 5 high
for( uint32_t i = 0; i < 500'000; ++i ){ asm( "nop" ); }
*PORTB = *PORTB & ~ ( 0b01 << 5 ); // make PORTB pin 5 low
for( uint32_t i = 0; i < 500'000; ++i ){ asm( "nop" ); }
}
}

## Slide 12: C style: derefenced pointer macro
#include <cstdint>
#define DDRB ( * (volatile uint8_t *) 0x24 )
#define PORTB ( * (volatile uint8_t *) 0x25 )
int main( void ){
DDRB = DDRB | ( 0b01 << 5 );
for(;;){
PORTB = PORTB | ( 0b01 << 5 );
for( uint32_t i = 0; i < 500'000; ++i ){ asm( "nop" ); }
PORTB = PORTB & ~( 0b01 << 5 );
for( uint32_t i = 0; i < 500'000; ++i ){ asm( "nop" ); }
}
}

## Slide 13: Using the manufacturers header
#include <cstdint>
#include "avr/io.h"
int main( void ){
DDRB = DDRB | ( 0b01 << 5 );
for(;;){
PORTB = PORTB | ( 0b01 << 5 );
for( uint32_t i = 0; i < 500'000; ++i ){ asm( "nop" ); }
PORTB = PORTB & ~( 0b01 << 5 );
for( uint32_t i = 0; i < 500'000; ++i ){ asm( "nop" ); }
}
}

## Slide 14: Abstraction
Let’s write a blink function! - But how do we pass the pin?
As a global definition
As an integer, enum, or another ‘closed’ value (C style)
As an object (OO)
As a class (Objects? No Thanks!)

## Slide 15: Using (global) macros
#define LED_DDR DDRB
#define LED_PORT PORTB
#define LED_MASK ( 0b01 << 5 )
void blink(){
LED_DDR = LED_DDR| ( 0b01 << 5 );
for(;;){
LED_PORT = LED_PORT | LED_MASK;
for( uint32_t i = 0; i < 500'000; ++i ){ asm( "nop" ); }
LED_PORT = LED_PORT & ~ LED_MASK;
for( uint32_t i = 0; i < 500'000; ++i ){ asm( "nop" ); }
}
}
Yes, ugly! But this is often used in Arduino libraries that need to be fast.

## Slide 16: Using an identifing value
enum class pin {
b0, b1, b2, b3, b4, b5, b6, b7,
c0, c1, c2, c3, c4, c5, c6, c7
};
void blink( pin p ){
pin_mode_output( p );
for(;;){
pin_write( p, 1 );
for( uint32_t i = 0; i < 500'000; ++i ){ asm( "nop" ); }
pin_write( p, 0 );
for( uint32_t i = 0; i < 500'000; ++i ){ asm( "nop" ); }
}
}
int main( void ){
blink( pin::b5 );
}
Widely used (Arduino wiring library)

## Slide 17: Using an identifing value - implementation
struct single_pin_info {
volatile uint8_t & direction;
volatile uint8_t & data;
uint8_t mask;
};
const single_pin_info pin_info [] = {
{ DDRB, PORTB, ( 0b01 << 0 ) },
...
{ DDRC, PORTC, ( 0b01 << 7 ) }
};
void pin_mode_output( pin p ){
auto info = pin_info[ static_cast< int >( p ) ];
info.direction = info.direction | info.mask;
}
void pin_write( pin p, bool value ){
auto info = pin_info[ static_cast< int >( p ) ];
if( value ){
info.data = info.data | info.mask;
} else {
info.data = info.data & ~ info.mask;
}
}

## Slide 18: Using an object
void blink( gpio & p ){
p.mode_output();
for(;;){
p.write( 1 );
for( uint32_t i = 0; i < 500'000; ++i ){ asm( "nop" ); }
p.write( 0 );
for( uint32_t i = 0; i < 500'000; ++i ){ asm( "nop" ); }
}
}
int main( void ){
auto led = gpio( pin::b5 );
blink( led );
}
Much less common (not C)

## Slide 19: Using an object - implementation
class gpio {
private:
const single_pin_info & info;
public:
gpio( pin p ): info( pin_info[ static_cast< int >( p ) ] ) {}
void mode_output() {
info.direction = info.direction | info.mask;
}
void write( bool value ){
if( value ){
info.data = info.data | info.mask;
} else {
info.data = info.data & ~ info.mask;
}
}
};

## Slide 20: Using a class
template< is_gpio P >
void blink(){
P::mode_output();
for(;;){
P::write( 1 );
for( uint32_t i = 0; i < 500'000; ++i ){ asm( "nop" ); }
P::write( 0 );
for( uint32_t i = 0; i < 500'000; ++i ){ asm( "nop" ); }
}
}
int main( void ){
blink< gpio< pin::b5 > >();
}

## Slide 21: Using a class - implementation
template< pin P >
class gpio {
private:
static constexpr const single_pin_info & info =
pin_info[ static_cast< int >( P ) ];
public:
static const bool gpio_marker = true;
static void mode_output() {
info.direction = info.direction | info.mask;
}
static void write( bool value ){
if( value ){
info.data = info.data | info.mask;
} else {
info.data = info.data & ~ info.mask;
}
}
};
template< typename T >
concept is_gpio = requires { T::gpio_marker; };

## Slide 22: Comparing passing mechanisms
Pass as | Blink code size | Style | Used | Extensible * | 0 overhead | Run-time flexible
macro | 218 | C | Ugly, but often used when speed is required | No * | Yes | No
identifier | 394 | C | Standard for non-OO | No | No * | Yes
object | 362 | C++, objects | Standard for OO | Yes | No * | Yes
class | 218 | C++, templates | Only used by some weirdo’s (Odin, Wouter, …) | Yes | Yes | No

## Slide 23: Q and maybe A?